Detailed construction directions:

Print out all templates (actual size) and these directions.

Cut out all the pieces from ½ inch pine or cedar.  You can use ¾ inch material but ½ inch is strongly preferred. The use of ¾ inch material may force you to change some dimensions.

Locate the center of the opening in the front wall (3 – 1/4 inches up from the bottom edge and centered left-to-right) then drill the 7/8 inch hole.

Locate and drill the a ¼ inch hole for the upper perch in each side piece as indicated on the original drawing.

If you plan to add a perch, drill a ¼ inch hole 2 inches up from the bottom edge and centered left-to-right then glue in a 2 inch long dowel.

Locate and drill the two screw holes in the front and back walls and set them with a countersink. If you do not have a countersink bit, carefully use a larger bit to make the bevel. Locate the holes in the center of the floor thickness.

Sand all pieces before assembly.

Cut the mitered angles on roof pieces at 22 degrees.

Position, glue, and nail the box top to the rear and front walls as shown in the original drawing.

Position the floor within the walls but do NOT glue or nail it.  Place a thin piece of plastic or cardboard between the floor and the back wall to keep a tiny space to allow removal of the floor after assembly. Tape the floor to the wall assembly.

Position, glue, and nail the wall assembly to the left wall as shown in the original drawing. Do NOT glue the floor in.

Position, glue, and nail the roof pieces to the left wall as shown in the original drawing. .)

*****NOTE *****There will be a small gap between the walls and the roof when the house is finished.

To prolong the life of the house, it is best, but not essential, to cover the roof with a roofing paper and light weight shingles.

Position, glue, and nail the right side to the assembly taking car to not glue the floor.

Remove the floor. You may need to tap in at an angle to remove it.

If the floor did not slide out easily, sand the edges until you have a very a loose fit.

Use four screws to install the house and allow you to clean it each fall.  Also, wax the screws before inserting them to make removal easier.

Add two medium sized eyehooks to the peak of the roof to facilitate hanging your birdhouse. A heavy-duty steel fishing leader works well for the hanging wire.

You can either leave the wood natural or paint it for a longer life.  However, do NOT finish the inside of the house.

Hang the house six to ten feet above the ground and in a location that is not ‘baked’ by the summer sun.

Enjoy your renters when they move in.